## Slide 1: IMPROVING DEMOLDING MANUFACTURING CONSTRAINTS FOR GRADIENT-BASED TOPOLOGY OPTIMIZATION WITHIN SIMULIA TOSCA STRUCTURE
Arvinth Shankar
Supervisors
Lisa-Marie Krauß
Thorsten Mertins, Peter Clausen

## Slide 2: AGENDA
MOTIVATION
INTRODUCTION
PROPOSED CONCEPT
RESULTS
CONCLUSION AND FUTURE STEPS

## Slide 3: MOTIVATION
Topology optimization sometimes result in structures that are not manufacturable, for example; by casting.
Cast restrictions are then applied to the optimization
Few methods are available to enforce cast restrictions. One such method is by parametrizing the design domain.
Aim - to modify and improve the parametrization in the current Tosca Structure inorder to obtain a clear and consistent castable result.
No casting restriction
Interior cavities make the model not demoldable
Casting
direction
With casting restriction
Castable
Not castable

## Slide 4: INTRODUCTION

## Slide 5: INTRODUCTION
ρ = F(P) [mapping]
Relative densities (ρ)
Element relative densities (ρ)
Parameters (P)
Element sensitivities
δΦ
δρ
Parameter sensitivities
δΦ
δP
Φ – design response
Optimizer
Optimized parameters (P)
Parameters are defined in a way to enforce casting constraint
δΦ
δρ
dΦ
dP
dρ
dP
=

## Slide 6: INTRODUCTION
OVERVIEW ON PARAMETERS
Relative densities of each element ρi
Apol - Pole area density
Lpol - Growth fraction for poles
Cpol - Carve fraction for poles
Poles
Finite elements
(Leiva et al., 2013)

## Slide 7: PROPOSED CONCEPT

## Slide 8: PROPOSED CONCEPT
CURRENT TOSCA, CUBOID CENTROIDS AND VOLUME FRACTION
Cuboid centroids
Volume fraction (Vf)
Mapping
Sensitivities
δΦ
δρ
dΦ
dP
dρ
dP
=
Vf taken into account
Vf taken into account
ρ = F(P)
belongs to pole 1
belongs to pole 2
pole 1
pole 2
pole 1
pole 2
Current Tosca

## Slide 9: PROPOSED CONCEPT
OVERVIEW ON FORMATION OF CUBOID POLES
1
2
3
Rotation of coordinate axis to point along cast direction
Projection of element centroids (rotated coordinate value) to each grid/pole
Sorting of element centroids in each pole along the cast direction
3d view
casting direction
centroids
x
y
z
x
z
y
2D projection plane
y
z
x

## Slide 10: PROPOSED CONCEPT
hemin
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
 | 1 | 1 | 1 | 1 | 1 | 0.5 | 0 | 0 | 0 | 0 | 0
ƒ3(Cpol)
hemax
0
1
Be(Cpol)
pole 2
pole 1
MAPPING BASED ON VOLUME FRACTIONS
ρe = ƒ1(Apol) x ƒ2(Lpol) x ƒ3(Cpol)
ρ = F(P)
→
Element i
ƒ1(Apol) = Vf Apol, Vf - volume fraction of an element inside a pole
ƒ1(Apol) = Vf, pole1 Apole1 + Vf, pole2 Apole2
i
1
2
ƒ2(Lpol) = Φ(He(Lpol))
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
 | 0 | 0 | 0 | 0 | 0 | 0.5 | 1 | 1 | 1 | 1 | 1
hemin
ƒ2(Lpol)
hemax
0
1
He(Lpol)
ƒ3(Cpol) = Φ(Be(Cpol))
3

## Slide 11: PROPOSED CONCEPT
dƒ3(Cpol)
dCpol
SENSITIVITY MAPPING
δΦ
δρ
dΦ
dP
dρ
dP
=
=
δΦ
δρ
dF(P)
dP
dΦ
dApol
=
δΦ
δρe
dF(Apol, Lpol, Cpol)
dApol
1
=
δΦ
δρe
dƒ1(Apol)
dApol
. ƒ2(Lpol) . ƒ3(Cpol)
dΦ
dLpol
=
δΦ
δρe
dF(Apol, Lpol, Cpol)
dLpol
2
=
δΦ
δρe
dƒ2(Lpol)
dLpol
. ƒ1(Apol) . ƒ3(Cpol)
=
δΦ
δρe
dF(Apol, Lpol, Cpol)
dCpol
3
=
δΦ
δρe
dƒ3(Cpol)
dCpol
. ƒ1(Apol) . ƒ2(Lpol)
Vf
dΦ
dCpol
Vf . Apole
Vf . Apole
Chart: 
| 0 | 2 | 3 | 4 | 5
 | 0 | 0 | 0 | 0 | 0
 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5
 | 0 | 0 | 0 | 0 | 0 | 0
0
hemin
hemax
dƒ2(Lpol)
dLpol
He(Lpol)
Chart: 
| 0 | 2 | 3 | 4 | 5
 | 0 | 0 | 0 | 0 | 0
 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5
 | 0 | 0 | 0 | 0 | 0 | 0
0
hemin
hemax
Be(Cpol)

## Slide 12: RESULTS

## Slide 13: RESULTS
OIL PAN MODEL (≈100K elements)
Boundary conditions
Load conditions
Cast direction
Optimization inputs
Objective : minimize compliance
Constraint : local volume ≤ 50%
Midplane : full design height
Frozen elements : Outer surface elements
Midplane - full design height
Cmin,Cmax
= 0
= 1
Lmin,Lmax
top
bottom

## Slide 14: OIL PAN MODEL
Chart: Iterations
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41
 | 5.1529e-06 | 4.5124e-06 | 4.1635e-06 | 3.7942e-06 | 3.4604e-06 | 3.2578e-06 | 3.1008e-06 | 2.9517e-06 | 2.8001e-06 | 2.6592e-06 | 2.5259e-06 | 2.4059e-06 | 2.3048e-06 | 2.219e-06 | 2.1438e-06 | 2.0752e-06 | 2.0137e-06 | 1.9597e-06 | 1.9179e-06 | 1.8867e-06 | 1.864e-06 | 1.8463e-06 | 1.8313e-06 | 1.8177e-06 | 1.8075e-06 | 1.7991e-06 | 1.7927e-06 | 1.7869e-06 | 1.7815e-06 | 1.7768e-06 | 1.7727e-06 | 1.769e-06 | 1.7654e-06 | 1.7618e-06 | 1.7584e-06 | 1.7557e-06 | 1.7536e-06 | 1.7516e-06 | 1.7493e-06 | 1.747e-06 | 1.7453e-06 | 1.7436e-06
Current Tosca
Cuboid centroids
Volume fraction
Chart: Iterations
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46
 | 5.1529e-06 | 4.5379e-06 | 4.2229e-06 | 3.8821e-06 | 3.5489e-06 | 3.359e-06 | 3.2287e-06 | 3.1252e-06 | 3.0131e-06 | 2.8963e-06 | 2.7926e-06 | 2.6965e-06 | 2.605e-06 | 2.5099e-06 | 2.4114e-06 | 2.3118e-06 | 2.2255e-06 | 2.1516e-06 | 2.0898e-06 | 2.0367e-06 | 2.0011e-06 | 1.9761e-06 | 1.9588e-06 | 1.9443e-06 | 1.9328e-06 | 1.9235e-06 | 1.9155e-06 | 1.909e-06 | 1.9024e-06 | 1.8951e-06 | 1.8887e-06 | 1.8816e-06 | 1.8748e-06 | 1.8696e-06 | 1.8653e-06 | 1.861e-06 | 1.8576e-06 | 1.8542e-06 | 1.8503e-06 | 1.8464e-06 | 1.8424e-06 | 1.8384e-06 | 1.8341e-06 | 1.8307e-06 | 1.8278e-06 | 1.8255e-06 | 1.824e-06
Chart: Iterations
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49
 | 5.1529e-06 | 4.5562e-06 | 4.2622e-06 | 3.9419e-06 | 3.6255e-06 | 3.4436e-06 | 3.3283e-06 | 3.2403e-06 | 3.1553e-06 | 3.0702e-06 | 2.9898e-06 | 2.9054e-06 | 2.8242e-06 | 2.7323e-06 | 2.6261e-06 | 2.5029e-06 | 2.3961e-06 | 2.3102e-06 | 2.2335e-06 | 2.1713e-06 | 2.1312e-06 | 2.106e-06 | 2.0886e-06 | 2.075e-06 | 2.0635e-06 | 2.0535e-06 | 2.0453e-06 | 2.038e-06 | 2.0309e-06 | 2.0241e-06 | 2.018e-06 | 2.0122e-06 | 2.0064e-06 | 2.0009e-06 | 1.9957e-06 | 1.9906e-06 | 1.9861e-06 | 1.982e-06 | 1.9782e-06 | 1.9746e-06 | 1.9707e-06 | 1.9673e-06 | 1.964e-06 | 1.9612e-06 | 1.9583e-06 | 1.9556e-06 | 1.9533e-06 | 1.9512e-06 | 1.949e-06 | 1.9475e-06
reference
- 4%
+ 7%
Obj value : 1.82 x 10-6
Obj value : 1.74 x 10-6
Obj value : 1.95 x 10-6

## Slide 15: OIL PAN MODEL
QUALITATIVE COMPARISON OF RESULTS
Centroid based – both current Tosca and cuboid centroids
ρpole1 ≈ 1
ρpole2 ≈ 0
Volume fraction based
ρpole1 ≈ 1
ρpole2 ≈ 0

## Slide 16: OIL PAN MODEL
PERFORMANCE COMPARISON FOR THREE METHODS (8 CPUs & 1 CPU)
Chart: Performance comparison (8 CPUs)
Current_tosca | 1.933 | 4.338 | 11.99 | 49.17
Cuboid_centroids | 1.476 | 2.418 | 4.301 | 9.896
Volume_fraction | 2.43 | 5.155 | 12.42 | 44.183
Current Tosca
Volume fraction with sparse storage
Cuboid centroids
Chart: Performance comparison (1 CPU)
 | 5.112 | 13.33 | 40.66 | 62.6
 | 2.908 | 5.67 | 11.287 | 26.3
 | 3.837 | 8.43 | 34.4 | 58.36
50k | 100k | 200k | 500k
50k | 100k | 200k | 500k
No. of elements
No. of elements

## Slide 17: STEERING MODEL (≈130k elements)
FE model and optimization inputs
Optimization inputs
Objective : minimize compliance
Constraint : local volume and volume
Midplane : variable height
Frozen elements : Outer surface elements
Midplane – variable height
Cmin,Cmax,Lmin
= 0
variable Lmax
top
bottom
Side view
Top view
3d view
Cast direction
Coupling constraint
Fixed B.C

## Slide 18: STEERING MODEL
Cuboid centroids
Volume fraction
Optimization with local volume ≤ 70%
Current Tosca
Rib height
design height
Midplane – variable height
design height
Rib height
Midplane – full design height

## Slide 19: STEERING MODEL
Cuboid centroids
Using volume fraction
Current Tosca
Optimization with local volume ≤ 33%

## Slide 20: CAR DOOR MODEL (≈500k elements)
FE model and optimization inputs
Cast direction
Optimization inputs
Objective : minimize compliance
Constraint : local volume ≤ 40%
Midplane : full design height
Design space : interior body below window
Midplane - full design height
Cmin,Cmax
= 0
= 1
Lmin,Lmax
top
bottom
Boundary conditions → pin supported at door hinges
Loading conditions → vertical force on door handle

## Slide 21: CAR DOOR MODEL
Current Tosca
Cuboid centroids
Using volume fraction
Optimization with local volume ≤ 40%
Relative vol : 53.58%
Relative vol : 53.26%
Relative vol : 52.88%

## Slide 22: COMPARISON OF RESULTS
Comparing quantities | Current Tosca | Cuboid centroids | Volume fraction
Low compliance value | ++ | ++ | +
Density plot distribution | ‒ | ‒ | +
Tosca Smooth | ‒ | ‒ | ++
Runtime performance | ‒ / + depending on fine/coarse mesh | ++ | ‒ / + depending on fine/coarse mesh
++
Optimal performance
+
Benefit
‒
Impact

## Slide 23: CONCLUSION AND FUTURE WORK

## Slide 24: CONCLUSION AND FUTURE WORK
CONCLUSION
Review and understand the current implementation.
Improve the existing code
Verified each functionality with appropriate unit tests.
Validated the implementation with industrial models.
- Modularized the existing code before new implementation.
Cuboid centroids
Volume fraction
- Compared the results qualitatively.
- Evaluated the runtime performance of new implementations.

## Slide 25: CONCLUSION AND FUTURE WORK
FUTURE WORK
Parting midplane :
  Elements are identified above and below midplane as positive and negative heights of their centroids.
  A single cuboid pole is formed and then split to two domains (above and below midplane)
  Bounds for parameter C will be zero ( Cmin = Cmax = 0 )
...
+ve heights
-ve heights
Midplane
1
2
3
4
Design
domain
Cast direction
A1, L1
A2, L2
Pole split to two
Parallelization for volume fraction calculation – to increase the runtime performance
Extension of algorithms to use different grids, e.g, a 2d tria grid (to capture intricacies)
...

## Slide 26: Thank you for your attention